## Slide 1: Energy and the Environment
Microgrids and Energy Communities
Dr Venizelos Efthymiou
efthymiou.venizelos@ucy.ac.cy

## Slide 2
The three objectives of the energy policy of EU

## Slide 3
"Accelerating Clean Energy Innovation" (COM(2016)763)
EU's global role
Funding Energy Science and Technology
Financial Instruments
Policy Signals
Policy Framework
Horizon Europe
Climate, Energy and Mobility
To meet the objectives of the Paris Agreement the Union will need to unlock scenarios for the transition towards net-zero GHG emissions economy including low-carbon technologies and strategies for decarbonisation.
Notes: Cli

## Slide 4: Europe advances with a more demanding target for achieving Paris Agreement
A new optimistic mandatory target of 32% RES energy use until 2030.
The energy mix is changing and the implementation of the energy transition to low carbon ones has started and it is speeding up.
This paradigm change introduces new technologies in the energy grid transforming it to active from passive at all voltages.

## Slide 5
The development of technologies supporting distributed architecture and the activation of the end users through effective technologies, generate the pre-requisites for the development of effective management of the energy resources of Communities for meeting their communal needs through the development of active participation with tangible benefits for all.
The evolution into energy communities generate the possibilities for optimal use of resources in coordination with the integrated grid which serves all.
Energy transition: The role of the active users and the development of the Energy Communities

## Slide 6: The binding rules of the Clean Energy Package for all Europeans are approved
Article 15: ‘active customer’ means a final customer or a group of jointly acting final customers who consume or store electricity generated within their premises located within confined boundaries or where allowed by Member States, on other premises, or sell self-generated electricity or participate in flexibility or energy efficiency schemes, provided that these activities do not constitute their primary commercial or professional activity;
Article 16: 'citizens energy community' means: a legal entity which is based on voluntary and open participation, effectively controlled by shareholders or members who are natural persons, local authorities, including municipalities, or small enterprises and microenterprises. The primary purpose of a citizens energy community is to provide environmental, economic or social community benefits for its members or the local areas where it operates rather than financial profits. A citizens energy community can be engaged in electricity generation, distribution and supply, consumption, aggregation, storage or energy efficiency services, generation of renewable electricity, charging services for electric vehicles or provide other energy services to its shareholders or members;
Notes: Trialogue: Commission, Council and Parliament
where relevant, a local energy community may conclude an agreement with a distribution system operator to which their network is connected on the operation of the local energy community's network;

## Slide 7: Energy communities need to overcome
SOCIAL CHALLENGES
TECHNICAL CHALLENGES

## Slide 8: Energy Directive and Energy communities
The text defines Local energy communities (LEC) with four main characteristics:
Autonomy & control
Open & voluntary membership
Democracy in governance & ownership
Payback for community
Member States shall provide and enable regulatory framework for LECs.

## Slide 9: Role of Operators in the case of LEC
Offer public infrastructure and connection
Support the freedom of choice of the consumer to join or not LECs.
Manage the LEC network
DSO as a neutral facilitator
LEC

## Slide 10: Energy communities’ technical goals
Increase RES & emerging technologies (storage) rate penetration.
Facilitate flexibility such as Demand Response schemes
Energy autonomy and self-sufficient regions.

## Slide 11: Energy communities’ social goals
Accelerate Reduction of greenhouse gas emissions
Energy equity
Energy security
Economic benefits-- Energy is moving from a commodity value to an exchange value.

## Slide 12: Energy communities open issues- Technology
Challenges regarding RES & emerging technologies integration.
  variability in large scale generation
  Reduced system inertia
  Distributed storage
Technological barriers to the Internet of Things (IoT).
Challenges regarding cyber security.

## Slide 13: Energy communities open issues- Market
Access to national electricity grids
to have non-discriminatory access to ‘all organized markets’ (e.g balancing) through a supplier or aggregator
how costs are shared out between the service provider, the consumer and the local or regional authorities, as well as the amount of subsidies available to finance investments.
Members of energy communities should also not be exempted from their responsibilities(should not receive exemption from taxes and levies) to avoid market distortion.
https://www.eurelectric.org/media/2458/local-energy-communities-final.pdf

## Slide 14: Energy communities open issues- Regulation
The rules for the internal governance &ownership structure of energy communities.
  How network charges are calculated for citizens
  energy communities vs renewable energy communities.
Discriminatory administrative burdens or costs in comparison with established energy companies should be lifted.
Services and technical solutions that exist or are currently being developed in the fields of management and demand response, as well as in the management of decentralised production should become priority.
https://www.interregeurope.eu/fPolicy_brief_Renewable_Energy_Communities

## Slide 15: How we address these issues
An inclusion definition for energy communities.
Facilitation to community participation in support schemes
Provisions that would guarantee market access in a non-discriminatory manner
The market design should require distribution tariffs and compensation to reward citizens and communities
Enhancing and promoting concepts such as microgrids or Web- of-cells.
Technology
Market
Regulation
https://www.ceer.eu/

## Slide 16: The bidirectional operation of storage system offer valuable flexibility services in the operation of the system
The operational needs of storage are complicated but their flexibility is of real value to the Operators!

## Slide 17
The energy mix is changing in support of sustainability

## Slide 18: Operational modes of a microgrid system

## Slide 19: What is a microgrid? (the definition that is the result of research work in EU)
Microgrids comprise LV distribution systems with distributed energy resources (DER) (microturbines, fuel cells, PV, etc.) together with storage devices (flywheels, energy capacitors and batteries) and flexible loads.
Such systems can be operated in a non-autonomous way, if interconnected to the grid, or in an autonomous way, if disconnected from the main grid.
The operation of microsources in the network can provide distinct benefits to the overall system performance, if managed and coordinated efficiently.

## Slide 20: A microgrid that connects a low voltage system

## Slide 21: Applications of microgrids
A microgrid connecting a low voltage feeder
A microgrid connecting a single house

## Slide 22: Operational layout of a microgrid

## Slide 23: Possible operators of a microgrid
DSO as flexibility actor
DSO as flexibility facilitator

## Slide 24: Dedicated microgrid operator

## Slide 25: Principles of centralised control

## Slide 26: Principles of decentralised control

## Slide 27: Frequency and voltage droops

## Slide 28: Control and management architecture of a multi-microgrid system
Notes: CAMC – Central Autonomous Management Controller

## Slide 29: Central autonomous management controller functionalities
Notes: CAMC – Central Autonomous Management Controller

## Slide 30: The control system should be able to balance between market participation and local needs

## Slide 31: Closed loop for energy markets – information exchange diagram

## Slide 32
Dr Venizelos Efthymiou
efthymiou.venizelos@ucy.ac.cy
Questions ?